## Slide 1: STEREO-VISION and Depth Estimation
Presented by: Ziwen Guo

## Slide 2: Stereo Vision Introduction 01
A quick overview of Stereo Vision and this Project

## Slide 3: Stereo-vision
Why stereo vision over monocular vision?
Depth Perception
Improved Accuracy and performances
3D Reconstruction
At a higher computational Cost and setup can be tricky

## Slide 4: Implementations and Project Setups
An overview on my project implementations, including calibration, rectification, and depth estimation using OpenCV
02

## Slide 5: Camera Setup
Dual Logitech HD Pro C920 webcam
  Easy to find, many used options
  Good performance (1080p 30FPS)
  Well Documented
Baseline: 9cm
Leveled to my best ability
Placed in a well-lit room during Calibration

## Slide 6: Sotware Setup
The software implementation is rather simple and straight forward with the help of OpenCV
Calibration
Rectification
Disparity calculation & Depth estimation

## Slide 7: Calibration
The calibration is performed using a 9x6 chessboard pattern with an inner-dimension of 8x5:
Reference Pictures taken and separated into left and right
Converted to grey scale
Optimal Camera matrices calculated individually
Stereo Calibration then performed to obtain translation and rotation matrices

## Slide 8: Difficulties
Despite the built-in chessboard detector’s conveniences, there are potential mistakes that can greatly affect the results
Blurry Images
Outliers
Exposure differences

## Slide 9: Rectification
Pairs the horizontal scan/epipolar lines
Matches the corresponding points
Calculate the lens distortion
Returns the corrected image

## Slide 10: Depth Estimation
Applies distortion calibration and new Camera matrices
Demo uses an existing face tracker
Calculates the estimated distance from the middle point of the bounding box using disparity
Supports multiple targets

## Slide 11: Quick Demonstration
A quick demo showing the project in action
03

## Slide 12: Quick Demo

## Slide 13: The END
Thank you for listening!
Do you have any questions?
Please keep this slide for attribution

## Slide 14: References
https://www.clearview-imaging.com/en/blog/stereo-vision-for-3d-machine-vision-applications
https://www.researchgate.net/figure/Stereo-vision-disparity_fig1_236455177
https://markhedleyjones.com/projects/calibration-checkerboard-collection
https://learnopencv.com/making-a-low-cost-stereo-camera-using-opencv/